# Overview on drill sections and surface units for 2023
### Surface unit #3
- Left behind at BEOICE.
### Surface unit #2 (use this one at EGRIP, 2023)
- Has newest 2023 software loading automatically on startup.
- To run old 2022 software, run in terminal bash /home/drill/surface-unit/drill-bootstrap-2022.sh
### Surface unit #1
- Identical to surface unit #2
- Has hardware error: depth display is unable to send values to PC but works otherwise fine (i.e. display values are correct).
---------------------
### Drill section #1 (use this one at EGRIP, 2023)
- This section uses the new 2023 drill orientation (BNO055) information, compatible with the new 2023 drill software started automatically on surface units #1 and #2 (bash /home/drill/surface-unit/drill-bootstrap.sh)
- Has been disassembled and reassembled after 2022 season.
- Has been tested in CPH and performs as expected.
### Drill section #2
- Section last used at EGRIP, 2022 (left behind at EGRIP; tested and worked then).
- Works only with old 2022 surface unit software: run bash /home/drill/surface-unit/drill-bootstrap-2022.sh
### Drill section #3
- Section last used at BEOICE, 2022/2023.
- New gear installed at BEOICE, 2022/2023.
- No changes otherwise made, and tested in CPH April, 2023, working as expected.
- Works only with old 2022 surface unit software: run bash /home/drill/surface-unit/drill-bootstrap-2022.sh