# Overview on drill sections and surface units for 2023
### Surface unit #3
- Left behind at BEOICE.
### Surface unit #2 (use this one for logger)
- Has newest 2023 software loading automatically on startup.
- Has problems starting the drill, but can communicate with drill (error raised only in field?)
- Uses MODBUS protocol for depth counter (needed by the logger).
### Surface unit #1 (use this one at EGRIP, 2023)
- Identical to surface unit #2 but uses CRLF protocal for depth counter (not useful for logger).
---------------------
### Drill section #1 (use this one at EGRIP, 2023)
- This section uses the new 2023 drill orientation (BNO055) information, compatible with the new 2023 drill software (available on surface units #1 and #2)
- Has been disassembled and reassembled after 2022 season.
- Has been tested in CPH and performs as expected.
- Works only with new 2023 surface unit software.
### Drill section #2
- Section last used at EGRIP, 2022 (left behind at EGRIP).
- Re-tested at EGRIP, 2023 (OK)
- Works only with old 2022 surface unit software.
### Drill section #3
- Section last used at BEOICE, 2022/2023.
- New gear installed at BEOICE, 2022/2023.
- No changes otherwise made, and tested in CPH April, 2023, working as expected.
- Works only with old 2022 surface unit software.